## Slide 1
"The Step Up"
B.Tech Graduate Internship — Project Report
Automated Dust & Defect Detection
for Camera Module Quality Inspection
Harsh Kumar
B.Tech (Software Engineering), Delhi Technological University
Intern, Samsung India Electronics — Camera Module Quality Inspection
Project Report
July 2026

## Slide 2
Agenda
SIEL create the future together!
01
Project Background
02
Objectives
03
Approach & Methodology
04
Work Completed
05
Current Status & Results
06
Live Demo
07
Challenges & Learnings
08
Future Work
2
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 3
Project Background
SIEL create the future together!
Mobile phone rear camera modules are optically inspected on the production line before assembly. Even microscopic contamination on the lens or sensor path — dust, glue residue, or stray fibre/thread — can cause visible defects in the final camera output, so every module must be screened at high throughput.
Why automate it?
Manual visual inspection is slow, subjective, and fatigue-prone at high line speeds
Contamination features are sub-pixel to a few pixels wide — hard for the eye to catch consistently
Production needs an objective, repeatable pass/fail (OK/NG) verdict per module
Inspection Setup
Basler industrial camera captures the module under controlled lighting
Region of Interest (ROI) isolated on the lens/sensor surface
Z-score based image processing flags anomalies
Operator confirms OK / NG verdict, stored for traceability
3
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 4
Objectives
SIEL create the future together!
Reliable Detection
Detect dust, glue-residue, and thread/fibre contamination on camera modules with a validated, explainable algorithm
Standalone Tool
Build a self-contained desktop application usable directly by line operators — no manual scripting
Configurable & Scalable
Support multiple camera models via per-model ROI and calibration configs, not a single hard-coded setup
Traceable Verdicts
Persist every OK / NG decision with the original and annotated image for audit and rework
4
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 5
Approach & Methodology
SIEL create the future together!
Core detection algorithm: local Z-score anomaly scoring
Z(x, y) = | I(x,y) − μ(x,y) | ⁄ σ(x,y)
μ, σ = local mean & std-dev from a boxFilter window • threshold = 3.0 • window = 31 px
Each pixel's intensity is compared against its local neighbourhood rather than a single global threshold — this keeps detection robust to uneven lighting and lens shading across the module surface. Pixels crossing the Z-score threshold are grouped into candidate blobs for classification.
Known trade-off: with window = 31 px, dust up to ~4 px radius is reliably caught; larger particles need a proportionally larger window — exposed as a tunable slider in the app.
Blob classification into 3 categories
Dust
Compact circular blobs → red-ring annotation
Glue Arc
Circularity + aspect-ratio gate, distance-transform stroke width for curved arcs → blue-ring annotation
Thread / Fibre
Distance-transform width ≤ 5 px → yellow-ring annotation
Contours found via cv2.findContours + minEnclosingCircle; non-dust detections are excluded from the reported dust count.
5
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 6
Work Done — The Application
SIEL create the future together!
A single-file Python desktop app (customtkinter + pypylon + OpenCV) built for direct operator use on the line.
Live Camera Feed
Basler / USB / synthetic-camera fallback; live feed downscaled for display, full-resolution capture used for inspection
Multi-ROI Selection
Circular multi-ROI selector per module region, with per-model ROI configs saved to disk
Calibration
Two-point (and four-method) calibration; physical size measured via max Feret length using the convex hull
Open Image Mode
Load previously captured images from disk and run detection / ROI / calibration on them, not just the live feed
Annotated Output
Red / blue / yellow ring annotations on both the live display and saved mask files, with a live dust count
OK / NG Workflow
Operator can flip the verdict; results stored in a model/original/NG-OK and model/after/NG-OK folder structure
6
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 7
Current Status
SIEL create the future together!
Working today
Validated Z-score detection (threshold 3.0, window 31) in production-usable form
All 3 defect categories (dust, glue, thread) classified and independently annotated
Full GUI workflow: camera enumeration → ROI → calibration → detection → OK/NG storage
Open-Image mode for offline review of previously captured modules
Open challenges
Blue AR-coating reflections and lens ring/donut artifacts remain persistent false-positive sources
Fixed 31 px window limits reliable dust detection to ~4 px radius; larger dust needs a larger window
3
Defect categories detected
31px
Z-score window size
3.0
Detection threshold
Detection history
The Z-score formula went through several regressions before settling on this externally-validated version, refined against real dust/glue/thread samples on the line.
Requirement carried through every iteration: the app must always support loading images from disk, not only the live feed.
7
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 8
Implementation Roadmap
SIEL create the future together!
Where we are, and the path to running this on the live inspection line
Phase 1
Algorithm R&D
Z-score detection formula researched, tuned, and validated (threshold 3.0, window 31)
Phase 2
App Development
Full desktop tool built: camera feed, ROI, calibration, 3-category classification, OK/NG storage
Phase 3
Pilot Validation
Running the tool against real modules offline; tuning against AR-reflection & ring-artifact false positives
Phase 4
Line Integration
Deploy the validated pipeline into the live inspection-line workflow alongside operators
Phase 5
Scale & Rollout
Extend per-model configs to additional camera-module variants across lines
Complete
In progress
Upcoming
8
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 9
Live Demo
SIEL create the future together!
Application walkthrough
Insert demo video here
(dust_inspector_final — live detection, ROI selection & OK/NG verdict flow)
9
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 10
Challenges & Learnings
SIEL create the future together!
Tuning is a trade-off
Sensitivity vs. false positives had to be balanced by hand across threshold, window size, and shape gates — no single setting worked for every module type
Look-alike artifacts
Lens ring/donut patterns and AR-coating reflections mimic real contamination and needed dedicated shape/circularity gates to filter out
Validated before shipped
The detection formula went through multiple regressions before arriving at the current externally-validated Z-score approach
Design for the operator
Per-model configs, an OK/NG override, and an offline Open-Image mode were built in from real line-usage needs, not as afterthoughts
10
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 11
Future Work
SIEL create the future together!
1
Adaptive window sizing
Auto-select or blend multiple window sizes so larger dust particles are caught without hand-tuning the slider
2
Cut false positives further
Additional gating for AR-coating reflections and lens ring artifacts beyond current shape filters
3
Line deployment
Move from validated desktop tool towards integration into the live inspection line workflow
4
Broader model coverage
Extend per-model ROI/calibration configs to additional camera-module variants as they come online
11
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 12
Thank You
Questions & Discussion
Harsh Kumar
Delhi Technological University • Samsung India Electronics