## Slide 1
"The Step Up"
B.Tech Graduate Internship — Project Report
Automated Dust & Defect Detection
for Camera Module Quality Inspection
Harsh Kumar
B.Tech (Software Engineering), Delhi Technological University
Intern, Samsung India Electronics — Camera Module Quality Inspection
Project Report
July 2026

## Slide 2
Agenda
SIEL create the future together!
01
Project Background
02
Objectives
03
Approach & Methodology
04
Work Completed
05
Current Status & Results
06
Live Demo
07
Challenges & Learnings
08
Future Work
2
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 3
Project Background
SIEL create the future together!
Mobile phone rear camera modules are optically inspected on the production line before assembly. Even microscopic contamination on the lens or sensor path — dust, glue residue, or stray fibre/thread — can cause visible defects in the final camera output, so every module must be screened at high throughput.
Why automate it?
Manual visual inspection is slow, subjective, and fatigue-prone at high line speeds
Contamination features are sub-pixel to a few pixels wide — hard for the eye to catch consistently
Production needs an objective, repeatable pass/fail (OK/NG) verdict per module
Inspection Setup
Basler industrial camera captures the module under controlled lighting
Region of Interest (ROI) isolated on the lens/sensor surface
Z-score based image processing flags anomalies
System assigns a PASS / FAIL verdict automatically, logged with barcode for traceability
3
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 4
Objectives
SIEL create the future together!
Reliable Dust Detection
Detect dust contamination on camera modules with a validated, explainable local Z-score algorithm
Operator-Safe Tool
Split into a read-only Operator window and a separate Teaching window, so line use can never accidentally edit ROIs
Configurable & Scalable
Named, savable ROI layouts per model/line, loaded and activated from Teaching — not a single hard-coded setup
Traceable Verdicts
Auto-assign PASS / FAIL per module and persist the source + annotated image and a CSV log for audit
4
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 5
Approach & Methodology
SIEL create the future together!
Core detection algorithm: local Z-score anomaly scoring
Z(x, y) = | I(x,y) − μ(x,y) | ⁄ σ(x,y)
μ, σ = local mean & std-dev from a boxFilter window • threshold = 3.0 • window = 100 px (default, tunable)
Each pixel's intensity is compared against its local neighbourhood rather than a single global threshold — this keeps detection robust to uneven lighting and lens shading across the module surface. Pixels crossing the Z-score threshold, inside the active ROI(s), form the raw candidate mask.
Scope today: the pipeline detects and flags dust only — it does not yet classify contamination into separate types (e.g. glue residue, thread/fibre). All accepted blobs are reported as one dust count.
Cleaning up the raw mask (single class: dust)
Morphological opening
3×3 elliptical kernel erases anything thinner than a few px — kills thin curved edge artifacts / arcs and 1–2 px sensor noise
Area + circularity gate
cv2.findContours + minEnclosingCircle; blobs below min-area (4 px²) or min-circularity (0.55) are rejected as noise or arc fragments
Optional mm-diameter gate
If two-point calibrated, diameter_px × mm/px is computed; blobs smaller than the min diameter (mm) are rejected too
Survivors are ringed in red with their size label (mm if calibrated, else px); any module with ≥1 accepted blob is flagged FAIL.
5
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 6
Work Done — The Application
SIEL create the future together!
A single-file Python desktop app (customtkinter + pypylon + OpenCV), redesigned into two windows to keep operator use foolproof.
Operator Window
Read-only live feed, status card, barcode entry, and a scrolling inspection log — nothing here is click-editable, by design
Teaching Window
Technician-only setup, opened separately: Model/Line naming, ROI + calibration canvas, detection params, camera settings
Named ROI Layouts
Circular multi-ROI placement on an interactive canvas (click, drag-pan, wheel-zoom); layouts saved and activated by name
Two-Point Calibration
Click two points at a known real-world distance; the resulting mm/px scale converts blob size to mm
Open Image Mode
Load previously captured images into the Teaching canvas to test ROI and detection settings offline
Auto Verdict + Logging
PASS/FAIL assigned automatically per module; source + annotated images and a CSV log are saved
6
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 7
Current Status
SIEL create the future together!
Working today
Validated Z-score dust detection (threshold 3.0, window 100) in production-usable form
Raw mask cleaned with morphological opening + area/circularity gates to reject arcs and noise
Two-window split shipped: read-only Operator view + interactive Teaching view for setup
Auto PASS/FAIL verdict, barcode logging, and Open-Image mode for offline review
Open challenges
Only dust is detected today — glue-residue and thread/fibre are not yet classified separately
Camera support is Basler-only via pypylon; no alternate/synthetic source if hardware is absent
1
Defect category detected
100px
Z-score window (default)
3.0
Detection threshold
Detection history
The Z-score formula went through several regressions before settling on this externally-validated version, refined against real dust/glue/thread samples on the line.
Requirement carried through every iteration: the app must always support loading images from disk, not only the live feed.
7
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 8
Implementation Roadmap
SIEL create the future together!
Where we are, and the path to running this on the live inspection line
Phase 1
Algorithm R&D
Z-score detection formula researched, tuned, and validated (threshold 3.0, window 31)
Phase 2
App Development
Two-window desktop tool built: read-only Operator view, Teaching setup, ROI/calibration, auto verdict + logging
Phase 3
Pilot Validation
Running the tool against real modules offline; tuning area/circularity gates against arc and noise false positives
Phase 4
Line Integration
Deploy the validated pipeline into the live inspection-line workflow alongside operators
Phase 5
Scale & Rollout
Extend per-model configs to additional camera-module variants across lines
Complete
In progress
Upcoming
8
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 9
Live Demo
SIEL create the future together!
Application walkthrough
Insert demo video here
(Operator window inspection flow, plus a look at ROI/calibration setup in the Teaching window)
9
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 10
Challenges & Learnings
SIEL create the future together!
Tuning is a trade-off
Sensitivity vs. false positives had to be balanced by hand across threshold, window size, and the area/circularity gates — no single setting worked for every module type
Look-alike artifacts
Thin curved edges and arc-shaped reflections mimic real dust; a morphological opening plus a circularity gate was needed to filter them out
Validated before shipped
The detection formula went through multiple regressions before arriving at the current externally-validated Z-score approach
The ROI editor was the real bug
A stray click on the operator's own feed could silently add or move an ROI — splitting it into a read-only view plus a separate Teaching view fixed it
10
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 11
Future Work
SIEL create the future together!
1
Multi-defect classification
Extend beyond dust-only detection to separately classify glue-residue and thread/fibre contamination, not just one combined count
2
Cut false positives further
Additional gating beyond the current area/circularity filters for edge and arc-shaped reflections
3
Line deployment
Move from validated desktop tool towards integration into the live inspection line workflow
4
Broader model coverage
Extend named ROI/calibration layouts to additional camera-module variants as they come online
11
Automated Camera-Module Defect Inspection — Samsung SIEL

## Slide 12
Thank You
Questions & Discussion
Harsh Kumar
Delhi Technological University • Samsung India Electronics